## Slide 1: Mini project
Final presentation
Instructed by – Professor Sekhar Mandal

## Slide 2: Pasumarthi Venkata siva sandeep
510519074
Semester 4

## Slide 3: Character segmentation
Main objective

## Slide 4: Morphological Image Operations
Dilation
Erosion
Opening
Closing

## Slide 5: Dilation
Dilation increases pixel density.
Used to increase the thickness of the font.

## Slide 6: Impact of Dilation
Before Dilation
After Dilation (4 X 4)

## Slide 7: Process to achieve dilation
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Make a duplicate array of same size and pixel values.
Now take structuring element from the user say (a, b).
Now parse the duplicate array from the top left corner to the right and go all the way to bottom.
When parsing, put the structuring element top left corner at the position you are say (x, y) and check the elements coinciding with the duplicate image array and structuring element.
If at any position the value of the duplicate image array is 1 then at position (x + a/2, y + b/2) put 2 and continue this process until parsing of total duplicate image array.
Now scan the duplicate image array once again and if at any position if you find 2 replace it by 1.
The final duplicate image array contains the dilated image using given structuring element.

## Slide 8: Erosion
Erosion decreases pixel density.
Used to thin the font.

## Slide 9: Impact of Erosion
Before Erosion
After Erosion (4 X 4)

## Slide 10: Process to achieve Erosion
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Make a duplicate array of same size and pixel values.
Now take structuring element from the user say (a, b).
Now parse the duplicate array from the top left corner to the right and go all the way to bottom.
When parsing, put the structuring element top left corner at the position you are say (x, y) and check the elements coinciding with the duplicate image array and structuring element.
If at any position the value of the duplicate image array is 0 then at position (x + a/2, y + b/2) put 2 and continue this process until parsing of total duplicate image array.
Now scan the duplicate image array once again and if at any position if you find 2 replace it by 0.
The final duplicate image array contains the eroted image using given structuring element.

## Slide 11: Opening
Used to open gaps in an image.

## Slide 12: Impact of Opening
Before Opening
After Opening (4 X 4)

## Slide 13: Process to achieve OPENING
After scanning and storing image in an array.
Take structuring element from the user.
Then perform erosion first and then dilation using given structuring element.
The final image array contain the opened image using given structuring element.

## Slide 14: Closing
Used to close gaps in an image.

## Slide 15: Impact of closing
Before Closing
After Closing (4 X 4)

## Slide 16: Process to achieve closing
After scanning and storing image in an array.
Take structuring element from the user.
Then perform dilation first and then erosion using given structuring element.
The final image array contain the closed image using given structuring element.

## Slide 18: Horizontal Projection Profile
Used to identify lines in an image.
Used to identify number of pixels and pixel density / distribution along rows.

## Slide 19: Horizontal profile of a line
Actual Line
Line’s Horizontal Profile

## Slide 20: Process to achieve horizontal projection profile
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Make a duplicate array of same size of original image and fill it with zeroes.
Calculate number of “1” pixels in each row and store it in an array.
In duplicate array now replace “0” pixels with number of “1” pixels stored in each row in above step.
Write the duplicate array values in the output file using proper format of .pbm file.

## Slide 21: Head Line Identification and Removal
Used to find the head lines in the image.

## Slide 22: Process to achieve head line removal method 1
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Perform horizontal projection profile on the original image.
From horizontal profile obtain text line information and store it in a text file.
In each text line calculate average number of pixels and find the first row of text line which is having number of pixel more than the average. Store the row number as headline in an array.
Remove the rows stored as head line and it’s consecutive 5 lines and it’s before line from the original image.
Finally write the stored image pixel values in .pbm format.

## Slide 23: Example of head line removal Method 1
Original Line
After Head Line Removal

## Slide 24: Process to achieve head line removal method 2
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Perform connected component labelling on original image and obtain the median width of label in each text line.
Use the structuring element with 1 row thick and median width long(wide) and perform opening operation on the image.
It will give us the head lines.
Then perform closing operation on the image performed after opening with a long line like structuring element.
Now remove the final image with the original image.
Finally write the stored image pixel values in .pbm format.

## Slide 25: Example of head line removal Method 2
Original Line
After Head Line Removal

## Slide 26: Example of head line Identification Method 2
Original Line
Identified Head Line

## Slide 27: Base Line Identification and Removal
Used to find the base lines in the image.

## Slide 28: Process to achieve Base line removal
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Perform horizontal projection profile on image and store the line information in a text file.
Now perform connected component labelling using the line information and obtain the median base line / row(median lower boundary) of labels in every text line and store it in an array. If any text line is having less than or equal to 3 labels we will take the base line of the previous text line.
Now remove stored base line rows in the original image.
Now write the stored pixel values in the output file in .pbm format.

## Slide 29: Example of Base line Identification
Original Line
Identified Base Line

## Slide 30: Final Objective – Character Segmentation
Used to segment characters which are used for training of ML/DL algorithm for optical character recognition (OCR) of Bengali scripts.

## Slide 31: Process to achieve character segmentation
Copy the original binary image in .pbm format.
Scan it and store the pixel values in an array.
Perform base line identification and obtain base line information.
Perform head line identification and obtain head line information
Then for each text line starting from the base line perform a vertical scan. During the scan if we get any obstacles(1 pixel) then either move left or right.
If you can’t move any where then calculate vertical distance from base line to your current position.
If the vertical distance is greater than or equal to the median height of the text line labels then perform a cut through the headline.
Do this for every text line.
Write the final array of pixels to the output file in .pbm format.

## Slide 32: Example of Character Segmentation
Original Line
After Character Segmentation

## Slide 33: For source code click below
Click Here

## Slide 34: Thank you